## Slide 1
ASAP · ROS 2 JAZZY · PYTHON
ROS 2 Basics
From a counter to a sensor
6 steps · 2 hours · keyboards on
/dht11_sim
/temperature
/env_validator
/env/validated
Notes: Welcome. Today every student writes, builds and runs ROS 2 nodes in Python. The diagram on the right is where we end up: a sensor node, a topic, a node that checks the data, and a topic with checked data.

## Slide 2
Today: six steps, one storyline
1
Workspace, package, node
A node that counts
18 min
2
Four ways nodes talk
turtlesim tour
15 min
3
Topics
Publisher + subscriber
20 min
4
Custom message
Count.msg
17 min
5
Someone else's package
DHT11 sensor
10 min
6
Validation service
Is the robot too hot?
25 min
Behind? bash ~/asap-kit/scripts/catchup.sh N
Check: bash ~/asap-kit/scripts/verify.sh N
Notes: Walk through the six steps. Every step adds to the same workspace. Point out the two scripts at the bottom: verify.sh checks a step, catchup.sh installs the finished version of a step if someone falls behind. Rule: a step running 5 minutes over, anyone still stuck runs catchup and moves on.

## Slide 3
0
Your group's channel
Same Wi-Fi, separate domains: you only see your own group's nodes
source ~/asap-kit/scripts/group_env.sh 3
bash ~/asap-kit/scripts/check_env.sh
EXPECT
PASS | ROS_DOMAIN_ID for your group | 13 = group 3
ALL GREEN: this laptop is ready.
Group 1
domain 11
Group 2
domain 12
Group 3
domain 13
Group 4
domain 14
Group 5
domain 15
Group 6
domain 16
Group 7
domain 17
Group 8
domain 18
Group 9
domain 19
group N → ROS_DOMAIN_ID = 10 + N
Notes: Everyone is about to run a node called /counter on the same Wi-Fi. ROS_DOMAIN_ID keeps groups apart. Every row must say PASS; the pyserial row may say WARN on student laptops. Instructor laptop uses domain 10.

## Slide 4
1
Workspace, package, node
Create a package and write a node that counts
18 min
Notes: Step 1. Goal: ros2 node list shows /counter.

## Slide 5
1
Workspace › package › node
~/ros2_ws
workspace
src/
counter_pkg/
package
package.xml
setup.py
counter_pkg/counter.py
ros2 run
/counter
node
Workspace
the folder you build in
Package
a unit of code: name, dependencies, nodes
Node
one running program with one job
Notes: Say: a robot is not one program; it is many small programs, called nodes, that talk. A package is how code is shipped and reused. You will install someone else's package in step 5.

## Slide 6
1
A robot is many small programs
Each box is a node. They talk over topics.
/camera_driver
/lidar_driver
/image
/scan
/planner
/cmd_vel
/motors
node one process, one job topic a named stream of messages
Notes: A camera driver and a lidar driver publish data; a planner combines them and publishes velocity commands; a motor node drives the wheels. Replace any one node without touching the others.

## Slide 7
1
Create the workspace and package
TYPE
mkdir -p ~/ros2_ws/src
cd ~/ros2_ws/src
ros2 pkg create counter_pkg \
--build-type ament_python \
--license Apache-2.0 \
--dependencies rclpy \
--node-name counter
Package name first. --dependencies takes every word after it.
YOU GET
counter_pkg/
├── package.xml dependencies
├── setup.py entry points
├── setup.cfg
├── resource/
├── counter_pkg/
│ ├── __init__.py
│ └── counter.py your node
└── test/
Notes: Type it live. Open the result in VS Code: code ~/ros2_ws. If ros2 pkg create complains that package_name is required, the name was placed after --dependencies.

## Slide 8
1
How ros2 run finds your code
One line in setup.py → entry_points → console_scripts
counter = counter_pkg.counter:main
counter
executable name
ros2 run counter_pkg counter
counter_pkg.counter
Python module
counter_pkg/counter.py
main
function
def main()
No executable found → check this line first, then rebuild.
Notes: entry_points in setup.py is how ros2 run finds your code. When ROS says "No executable found", look here first. Any change to setup.py needs colcon build.

## Slide 9
1
counter.py: four TODOs
cp ~/asap-kit/starter/step1/counter.py ~/ros2_ws/src/counter_pkg/counter_pkg/
class Counter(Node):
def __init__(self):
super().__init__('counter') # 1.1
self.count = 0
self.timer = self.create_timer(1.0,
self.on_timer) # 1.2
def on_timer(self):
self.count += 1 # 1.3
self.get_logger().info(f'count = ...')
def main(args=None):
rclpy.init(args=args)
node = Counter()
rclpy.spin(node) # 1.4
1.1
Name the node
'change_me' → 'counter'
1.2
Timer
call on_timer every 1.0 s
1.3
Callback
count up and log
1.4
Spin
rclpy.spin is the loop
Notes: Walk through counter.py top to bottom: class, __init__, timer, callback, main, spin. Do 1.1 together, students do 1.2-1.4. Point out: there is no while True. rclpy.spin is the loop; the timer calls your code.

## Slide 10
1
Build, source, run
cd ~/ros2_ws
colcon build --symlink-install
source install/setup.bash
ros2 run counter_pkg counter
OUTPUT
[INFO] [...] [counter]: count = 1
[INFO] [...] [counter]: count = 2
[INFO] [...] [counter]: count = 3
Every new terminal: source ~/ros2_ws/install/setup.bash
REBUILD?
You changed | Rebuild
a .py node | no, restart it
setup.py, package.xml, new file | yes
.msg / .srv / CMakeLists.txt | yes + source
--symlink-install links your .py files into install/
Notes: --symlink-install means editing a .py file needs no rebuild, only a restart. setup.py, package.xml and interface files need colcon build. Package not found: source install/setup.bash in that terminal.

## Slide 11
1
Look inside a running system
ros2 node list
ros2 node info /counter
rqt_graph
/counter
rqt_graph
/counter
EXTENSION
ros2 run counter_pkg counter \
--ros-args -r __node:=counter2
Same code, two nodes: /counter and /counter2
CHECKPOINT
You edited counter.py, then setup.py. Which one needed a rebuild?
Notes: Checkpoint answer: setup.py. With --symlink-install, .py files are linked; setup.py, package.xml and interfaces need colcon build. Common errors: Package not found (not sourced); /change_me in node list (TODO 1.1).

## Slide 12
2
The four ways nodes talk
A tour on turtlesim, from the command line
15 min
Notes: Step 2. No code. Students explore turtlesim with the CLI. Done when everyone has spawned turtle2.

## Slide 13
2
Four ways nodes talk
Topic
a stream: publish, anyone subscribes, no reply
/turtle1/pose
A
B
C
Service
one request, one response
/spawn
A
B
request
response
Parameter
a named setting, changeable while running
background_r
node
background_r = 150
Action
a long job: feedback, result, cancel
/turtle1/rotate_absolute
A
B
goal
feedback… result
Notes: Nodes are the smallest unit; everything else is how they talk. Four ways, all met today at the command line on a node someone else wrote. Topics stream, services answer once, parameters are settings, actions are long jobs with progress and cancel.

## Slide 14
2
turtlesim tour
ros2 run turtlesim turtlesim_node # terminal 1
ros2 run turtlesim turtle_teleop_key # terminal 2: arrow keys drive
TOPIC
ros2 topic list -t
ros2 topic echo /turtle1/pose
SERVICE
ros2 service list -t
ros2 service call /spawn turtlesim/srv/Spawn "{x: 2.0, y: 2.0, theta: 0.0, name: turtle2}"
PARAM
ros2 param list /turtlesim
ros2 param set /turtlesim background_r 255
ACTION
ros2 action send_goal --feedback /turtle1/rotate_absolute \
turtlesim/action/RotateAbsolute "{theta: 1.57}"
Notes: Show the first few commands yourself, then hand over to the questions on the next slide. The background colour only changes after ros2 service call /clear std_srvs/srv/Empty.

## Slide 15
2
Your turn: answer at the terminal
# | Question | Hint
2.1 | Which node sends commands to turtlesim, on which topic? | rqt_graph, ros2 node list
2.2 | Type of /turtle1/pose? Its fields? | ros2 topic list -t, ros2 interface show
2.3 | Where is the turtle now? | ros2 topic echo /turtle1/pose
2.4 | Drive in a circle without the keyboard | ros2 topic pub -r 1 /turtle1/cmd_vel ...
2.5 | Add turtle2 at (2, 2) | ros2 service call /spawn ...
2.6 | What does /spawn take and return? | ros2 interface show turtlesim/srv/Spawn
2.7 | Make the background red | ros2 param set ... then /clear
2.8 | Rotate to face up, watch the progress | ros2 action send_goal --feedback ...
Full commands: STUDENT_HANDBOOK.md, step 2
Notes: Answers: 2.1 /teleop_turtle publishes on /turtle1/cmd_vel 2.2 turtlesim/msg/Pose: x, y, theta, linear_velocity, angular_velocity (float32) 2.3 starts at x 5.544, y 5.544, theta 0.0 2.4 topic pub -r 1 runs until Ctrl+C 2.5 Spawn_Response(name='turtle2'); /turtle2/... topics appear 2.6 request x, y, theta, name; response name 2.7 colour changes only after /clear: the node decides when to apply the parameter 2.8 Feedback remaining..., then Result delta..., SUCCEEDED

## Slide 16
2
Checkpoint: which pattern?
The turtle's position, 30 times a second
?
Add a turtle
?
Change the background colour
?
Turn 180° and know when it is done
?
Notes: Ask the room before showing the next slide.

## Slide 17
2
Which pattern? Answers
The turtle's position, 30 times a second
Topic
Add a turtle
Service
Change the background colour
Parameter
Turn 180° and know when it is done
Action
Notes: Topic; service; parameter; action.

## Slide 18
3
Topics
The counter publishes; a listener subscribes
20 min
Notes: Step 3. Goal: the listener prints "heard N".

## Slide 19
3
Publisher → topic → subscriber
/counter
/count
std_msgs/msg/Int32
/count_listener
publisher
subscriber
They connect when
NAME and TYPE match
Neither knows the other exists.
Mismatch
silence, no error
Check with ros2 topic list -t
Notes: A publisher and a subscriber never meet. ROS matches them by topic name and message type. Get either wrong and nothing flows, with no error.

## Slide 20
3
Every message has a type
ros2 interface show std_msgs/msg/Int32
# This was originally provided as an example message.
# It is deprecated as of Foxy
# It is recommended to create your own
# semantically meaningful message.
# ...
int32 data
“create your own semantically meaningful message”
→ that is step 4
For now: one field, data, an int32.
Notes: Show the interface and read the comment out loud. Hold that thought until after the break.

## Slide 21
3
Your turn: TODO 3.1 – 3.7
cp ~/asap-kit/starter/step3/*.py ~/ros2_ws/src/counter_pkg/counter_pkg/
TODO | File | Write
3.1 | counter.py | from std_msgs.msg import Int32
3.2 | counter.py | create_publisher(Int32, 'count', 10)
3.3 | counter.py | msg = Int32(); msg.data = ...; publish
3.4 | count_listener.py | create_subscription(Int32, 'count', ...)
3.5 | count_listener.py | log msg.data
3.6 | setup.py | second entry point
3.7 | package.xml | <depend>std_msgs</depend>
SETUP.PY (3.6)
'console_scripts': [
'counter = counter_pkg.counter:main',
'count_listener = ...',
],
Mind the comma between entries.
cd ~/ros2_ws
colcon build --symlink-install
source install/setup.bash
Notes: Do 3.1-3.3 (the publisher) live on the projector. Students do 3.4-3.7. setup.py changed, so rebuild. Errors: build error in setup.py (missing comma); No executable found for count_listener (entry point missing or no rebuild); listener silent (topic name typo, or other terminal not sourced).

## Slide 22
3
Inspect the topic
ros2 topic list -t
/count [std_msgs/msg/Int32]
/parameter_events [...]
/rosout [...]
ros2 topic echo /count --once
data: 7
---
ros2 topic hz /count
average rate: 1.000
min: 0.997s max: 1.002s
ros2 topic info /count
Type: std_msgs/msg/Int32
Publisher count: 1
Subscription count: 1
rqt_graph → dropdown Nodes/Topics (active): /counter → /count → /count_listener
Notes: Run counter and count_listener in two terminals, inspect from a third. In rqt_graph switch the dropdown to Nodes/Topics (active) and refresh.

## Slide 23
3
Pretend to be the counter
ros2 topic pub --once /count \
std_msgs/msg/Int32 "{data: 999}"
LISTENER
[count_listener]: heard 3
[count_listener]: heard 999
[count_listener]: heard 4
Also try: a second listener, then ros2 topic info /count
CHECKPOINT
999 came from the command line, and the listener printed it. Who can publish on a topic?
Notes: Checkpoint answer: any node on the same domain with the same name and type. The subscriber cannot tell who sent it. That is also why each group has its own ROS_DOMAIN_ID.

## Slide 24
Break
5 minutes
Next: your own message type
Notes: During the break: plug in the Arduino and check /dev/ttyACM0 on the instructor laptop.

## Slide 25
4
Your own message
Replace Int32 with Count: what, who, when
17 min
Notes: Step 4. Goal: ros2 topic echo /count shows source: counter.

## Slide 26
4
A number vs a meaningful message
std_msgs/msg/Int32
int32 data
a number
asap_interfaces/msg/Count
int64 count
string source
builtin_interfaces/Time stamp
what, who, when
Messages are the contract between nodes, and often between teams.
Notes: Int32 is a number. Count is what was counted, by whom, and when.

## Slide 27
4
An interface package
ament_cmake: the interface code generator runs under CMake
msg/Count.msg
colcon build
asap_interfaces.msg.Count
(Python + C++)
counter_pkg
<depend>asap_interfaces</depend>
TYPE
cd ~/ros2_ws/src
ros2 pkg create asap_interfaces --build-type ament_cmake --license Apache-2.0
cd asap_interfaces && rm -r include src && mkdir msg
cp ~/asap-kit/starter/step4/Count.msg msg/ # TODO 4.1: write the three fields
Notes: This is the one package that is CMake instead of Python, because the interface code generator runs under CMake. The classes it generates are used from Python.

## Slide 28
4
TODO 4.2 and 4.3: wire up the generator
CMakeLists.txt
# under find_package(ament_cmake REQUIRED)
find_package(builtin_interfaces REQUIRED)
find_package(rosidl_default_generators REQUIRED)
rosidl_generate_interfaces(${PROJECT_NAME}
"msg/Count.msg"
DEPENDENCIES builtin_interfaces
)
package.xml
<!-- under <buildtool_depend>ament_cmake -->
<buildtool_depend>rosidl_default_generators
</buildtool_depend>
<depend>builtin_interfaces</depend>
<exec_depend>rosidl_default_runtime
</exec_depend>
Just above <export>:
<member_of_group>rosidl_interface_packages
</member_of_group>
cd ~/ros2_ws && colcon build --symlink-install
ros2 interface show asap_interfaces/msg/Count
The first interface build takes about 30 s.
Notes: Errors: Unknown CMake command rosidl_generate_interfaces (missing find_package); xmllint error (member_of_group must be just above <export>); builtin_interfaces/Time unknown (missing DEPENDENCIES or <depend>). Warn them the build takes about 30 s.

## Slide 29
4
Use it: TODO 4.4 – 4.6
cp ~/asap-kit/starter/step4/*.py ~/ros2_ws/src/counter_pkg/counter_pkg/
TODO | File | Write
4.4 | counter.py | publish Count: count, source, stamp
4.5 | count_listener.py | subscribe with Count; log count, source
4.6 | package.xml | <depend>asap_interfaces</depend>
msg.source = self.get_name()
msg.stamp = self.get_clock().now().to_msg()
TRY: new counter, old listener
$ ros2 topic list -t
/count [asap_interfaces/msg/Count,
std_msgs/msg/Int32]
One name, two types: nothing flows, no error. Then do 4.5.
Notes: Mismatch demo: run the new counter (Count) with the old listener (Int32). The listener receives nothing and there is no error. ros2 topic list -t shows one name with two types. Then fix the listener.

## Slide 30
4
Check
ros2 topic echo /count --once
count: 6
source: counter
stamp:
sec: 1790210130
nanosec: 733066021
---
LISTENER
[count_listener]: heard 1 from counter
[count_listener]: heard 2 from counter
CHECKPOINT
You added a field to Count.msg. What needs rebuilding?
Notes: Checkpoint answer: asap_interfaces and every package that uses it, then re-source. colcon build from the workspace root does both. Errors: No module named asap_interfaces (not built or not re-sourced); AttributeError data (a Count has count, not data).

## Slide 31
5
Someone else's package
A DHT11 temperature and humidity sensor
10 min
Notes: Step 5. Goal: ros2 topic list -t shows /temperature and /humidity.

## Slide 32
5
Using a package you did not write
Find out what it does from the outside
git clone
get the code
rosdep install
its dependencies
colcon build
build it
inspect
topics, types, params, README
YOUR TURN
cd ~/ros2_ws/src
git clone https://github.com/praiseorji4/dht11_ros.git
cd ~/ros2_ws && colcon build --symlink-install && source install/setup.bash
ros2 launch dht11_ros dht11.launch.py
No internet? cp -r ~/asap-kit/vendor/dht11_ros ~/ros2_ws/src/
Notes: Most robot software is packages you did not write: drivers, maps, planners. The skill is to plug one in and find out what it does from the outside: topics, types, parameters and its README. Open https://github.com/praiseorji4/dht11_ros on the projector and walk the README before they clone. rosdep install is skipped: the simulator needs no extra dependencies.

## Slide 33
5
Real sensor or simulator: same topics
DHT11
Arduino
USB serial
T:24.0,H:55.0
/dht11_serial
instructor
/dht11_sim
students
/temperature
sensor_msgs/msg/Temperature °C
/humidity
sensor_msgs/msg/RelativeHumidity 0-1
ros2 launch dht11_ros dht11.launch.py # simulated
ros2 launch dht11_ros dht11.launch.py mode:=serial port:=/dev/ttyACM0 # real
Notes: Demo first on the projector with the real sensor (terminal with ~/demo_ws sourced): ros2 launch dht11_ros dht11.launch.py mode:=serial port:=/dev/ttyACM0 ros2 topic echo /temperature --field temperature Warm the sensor with your fingers or breath. Students run the simulator: same topics, same types, so their code works with either. Hardware fails: switch to the simulator.

## Slide 34
5
Your turn: answer at the terminal
# | Question | Hint
5.1 | Which node did the launch start? | ros2 node list
5.2 | Topics and types? | ros2 topic list -t
5.3 | One temperature message? | ros2 topic echo /temperature --once
5.4 | Unit of humidity? | ros2 interface show sensor_msgs/msg/RelativeHumidity
5.5 | How often? | ros2 topic hz /temperature
5.6 | What can you tune? | ros2 param list /dht11_sim
5.4
relative_humidity: 0.594
59.4 %
The message defines humidity as a fraction, 0.0 to 1.0. Read the interface.
Notes: Answers: 5.1 /dht11_sim (instructor: /dht11_serial) 5.2 /temperature [sensor_msgs/msg/Temperature], /humidity [sensor_msgs/msg/RelativeHumidity] 5.3 header (stamp, frame_id: dht11), temperature, variance 0.0 5.4 fraction 0.0-1.0: 0.594 = 59.4 % 5.5 average rate 1.000 (real sensor 0.5 Hz) 5.6 base_humidity, frame_id, glitch_rate, rate_hz, target_temperature Checkpoint: the DHT11 is replaced by a better sensor with a different driver. What changes in your code? Nothing, if the new driver publishes the same topic and type.

## Slide 35
6
Is the robot too hot?
A validation service with a threshold
25 min
Notes: Step 6. Goal: valid: false appears on /env/validated after heating the simulator.

## Slide 36
6
The DHT11 measures the robot
Every reading gets a verdict
max_temp
35.0 °C
a parameter: change it while the robot runs
temperature is NaN
valid: false
no reading (the sensor did not answer)
temperature > max_temp
valid: false
temperature 40.0 C is above max_temp 35.0 C
otherwise
valid: true
reason: ''
Notes: The sensor reports a temperature. Whether it is safe is a separate decision with its own owner: the validator service. The limit lives in one place, as a parameter.

## Slide 37
6
The pipeline
/dht11_sim
/humidity
/temperature
/env_validator
/validator_server
request: temperature
valid, reason
max_temp = 35.0
/env/validated
stamp
temperature
humidity
valid
reason
Every reading is published, with its verdict. Listeners decide what to do.
Notes: Too-hot readings are published too, marked valid: false. A too-hot reading is the overheating signal. With the verdict attached, listeners can slow down, stop, or raise an alarm without asking the validator again.

## Slide 38
6
TODO 6.1: the interfaces
srv/ValidateReading.srv (6.1a)
float64 temperature # request
---
bool valid # response
string reason
msg/EnvReading.msg (6.1b)
builtin_interfaces/Time stamp
float64 temperature
float64 humidity
bool valid
string reason
CMakeLists.txt (6.1c)
rosidl_generate_interfaces(${PROJECT_NAME}
"msg/Count.msg"
"msg/EnvReading.msg"
"srv/ValidateReading.srv"
DEPENDENCIES builtin_interfaces)
cd ~/ros2_ws/src/asap_interfaces && mkdir srv
cp ~/asap-kit/starter/step6/ValidateReading.srv srv/
cp ~/asap-kit/starter/step6/EnvReading.msg msg/
Notes: Do 6.1 together: the .srv file, the two EnvReading verdict fields, the CMake list, rebuild, ros2 interface show asap_interfaces/srv/ValidateReading.

## Slide 39
6
The server: TODO 6.2 – 6.3
ros2 pkg create env_monitor --build-type ament_python --license Apache-2.0 \
--dependencies rclpy sensor_msgs asap_interfaces --node-name validator_server
cp ~/asap-kit/starter/step6/*.py env_monitor/env_monitor/
TODO | Write
6.2 | create_service(ValidateReading, 'validate_reading', ...)
6.3 | NaN → False · > max_temp → False + reason · else True
ros2 service call /validate_reading \
asap_interfaces/srv/ValidateReading "{temperature: 40.0}"
AFTER 6.2, BEFORE 6.3
valid=True, reason=
'not checked yet: TODO(6.3)'
AFTER 6.3
valid=False, reason=
'temperature 40.0 C is above max_temp 35.0 C'
Notes: Do 6.2 live and call the service before 6.3: it accepts 40 °C. Then students do 6.3. {temperature: 25.0} returns valid=True.

## Slide 40
6
The client: TODO 6.4 – 6.8
TODO | Write
6.4 | subscribe 'temperature' (Temperature), 'humidity' (RelativeHumidity)
6.4b | humidity_pct = relative_humidity * 100.0
6.5 | create_client(ValidateReading, 'validate_reading'); wait_for_service
6.6 | call_async(request); add_done_callback(...)
6.7 | copy valid + reason into the reading; publish EVERY reading
6.8 | setup.py: 'env_validator = env_monitor.env_validator:main',
Inside a callback
call_async
never the blocking call(). It waits for an answer that can never arrive.
Rebuild and source after 6.8.
Notes: A blocking call() inside a callback waits for an answer that the stuck node itself would have to deliver. call_async plus a done-callback is the pattern. Errors: humidity 0.62 on the topic (forgot x100); log NOT OK but only valid: true on the topic (6.7 filters); env_validator freezes after one reading (blocking call).

## Slide 41
6
Heat the robot
Chart: Simulated temperature after target_temperature 40.0 (1 reading/s)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35
temperature (°C) | 27.1 | 26.9 | 27 | 26.9 | 27 | 26.9 | 27.1 | 27.6 | 28 | 28.6 | 29.2 | 29.8 | 30.4 | 30.9 | 31.3 | 31.9 | 32.3 | 32.7 | 33.1 | 33.6 | 33.9 | 34.6 | 35.2 | 35.5 | 35.9 | 36.5 | 36.9 | 37.4 | 37.8 | 38.3 | 39.1 | 39.6 | 40.1 | 40.1 | 40 | 40
max_temp | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35
ros2 param set /dht11_sim target_temperature 40.0
ENV_VALIDATOR
ok 33.9 C 62.1 %
ok 34.6 C 62.7 %
NOT OK temperature 35.2 C
is above max_temp 35.0 C
NOT OK temperature 35.5 C ...
RAISE THE LIMIT, LIVE
ros2 param set /validator_server \
max_temp 45.0
Decimals only: 45.0, not 45
Notes: Four terminals: launch dht11_ros, run validator_server, run env_validator, echo /env/validated. Then heat the sim. From 27 °C it crosses 35 °C in about 16 s. Then raise max_temp to 45.0 and the readings are ok again, with no restart.

## Slide 42
6
ros2 topic echo /env/validated
NORMAL
temperature: 26.9
humidity: 62.2
valid: true
reason: ''
TOO HOT
temperature: 40.1
humidity: 64.0
valid: false
reason: temperature 40.1 C is
above max_temp 35.0 C
CHECKPOINT
A reading is valid: false. Why publish it instead of dropping it?
Notes: Checkpoint answer: it is the overheating signal. Dropping it hides it from every other node; with the verdict attached, listeners can act without asking the validator again. Extension: an overheat_alarm node that logs an error when valid changes from true to false.

## Slide 43
Your pipeline, on the real sensor
ros2 launch dht11_ros dht11.launch.py mode:=serial port:=/dev/ttyACM0
ros2 run env_monitor validator_server --ros-args -p max_temp:=30.0
ros2 run env_monitor env_validator
ros2 topic echo /env/validated
Hold the sensor → valid: false. Let go → valid: true.
Same nodes you wrote against the simulator, unchanged.
Notes: On the instructor laptop with ~/demo_ws sourced in every terminal (optionally copy a group's env_monitor into ~/demo_ws/src and rebuild). Set max_temp 1-2 °C above the room reading; a hand raises a DHT11 by only a few degrees.

## Slide 44
Four ways nodes talk: today's examples
Topic
/count /temperature /env/validated
steps 3, 5, 6
Service
/validate_reading /spawn
steps 2, 6
Parameter
max_temp target_temperature background_r
steps 2, 5, 6
Action
/turtle1/rotate_absolute
step 2 · write one next time
Notes: Close with the four patterns, one line each, pointing at the cheat sheet. Actions: written next time.

## Slide 45
Keep going
CHEATSHEET.md
every command from today, one page
STUDENT_HANDBOOK.md
steps, TODOs, expected output, fixes
verify.sh N
check a step
catchup.sh N
install the finished step
Next time: actions
Notes: Point to the cheat sheet and handbook. Next session: writing an action server and client.